[i]MUSIC, SCIENCE AND TECHNOLOGY: DISSCO, AN INTERDISCIPLINARY PROJECT

Rishabh RAJAGOPALAN, Xuqing SUN, Sever TIPEI, Shenyi WANG

National Center for Supercomputer Applications,
Computer Music Project
University of Illinois

A Digital Instrument for Sound Synthesis and Composition, DISSCO combines composition and sound design in a unified approach. It has three main components: LASS, a Library for Additive Sound Synthesis, the synthesis engine, CMOD, a Composition Module and LASSIE, a Graphic User Interface. CMOD is a tree, a directed graph with parent-children relations between its levels, a hierarchical architecture that mirrors the structural elements of a composition. DISSCO was conceived as a "Rolls Royce bulldozer", precise, detailed control coupled with brute force: CMOD can handle an arbitrary number of sounds with an arbitrary number of partials each. Their characteristics (frequency, amplitude, FM, AM, transients, location in space, reverberation, etc.) can be selected through deterministic procedures (choosing from a list, using patterns, sieves, etc.) or through chance operations (probability density functions, stochastic distributions, Markov chains, etc.). Such tools could be applied at different time scales (piece, section, sound, frequency) and the link between the computer-assisted composition and sound design is seamless. At the same time, DISSCO can produce compositions for acoustic instruments and voices to be notated in standard score format.

DISSCO is comprehensive in the sense that it delivers a final product which does not require further adjustments. It is a “black box” in the sense that it reads in the data provided by the user and outputs a finished object, the piece, in a uninterrupted process. This is necessary in order to preserve the integrity of the operation: modifying the results or intervening during the computations would amount to the alteration of the data or of the logic embedded in the software, a falsification of the experiment.

Meanwhile, by simply changing the seed for the random number generator, DISSCO can generate manifold compositions. A manifold compositions consist of all actual and potential variants of a work that contains elements of indeterminacy and is generated by a computer reading the same data for each variant. Unique versions of the same piece, such variants share the same structure and are the result of the same process but differ in the way specific events are actualized. The differences can range from a slight re-arrangement of the notes in the score or of computer-generated sounds in time, to radical alterations of textures and even of the formal architecture of the piece. Similar to faces in a crowd, the members of the manifold are distinct while sharing basic, common features: all conceivable outcomes are equally valid results of an abstract blueprint and a related process.

By potentially creating large numbers of unique versions of the same archetype and thus mass producing distinct variants of a work, manifold compositions represent an idiomatic way of using computers in music. The process requires the availability of comprehensive software that does not allow the intervention of the user once the computations have started. The model promotes pre-composition planning along with an experimental and speculative attitude. DISSCO and its features have been described in more detail in the past [1]. The paper presents three recent additions to the project.

Perceived distance of the sound source.
On top of a current version of DISSCO, we added another feature to realize the perceived distance of a sound with given frequency and loudness. Under the same loudness, the perceived distance is decided by the softness of sound; whispering from a small distance and shouting from a large distance could be distinguished even they may have the same loudness and frequency at terminal point. We looked through research in vocal area and realized that the main factors influencing perceived vocal effort are the spectral shape of the sound and the reverberation effect. Variation in spectral envelope can change the brightness of the sound, thus human brain can use past experience to process how soft or solid the sound is.

We found that very few researches have been conducted regarding to the acoustic features of music voices at different effort level, while quite a few researches regarding speech recognition and synthesis have been done in the vocal area. Zhang and Hansen [2] analyzed speech data with five modes of vocal effort and found that frame energy distribution and spectral tilt are noticeable factors that differ between one vocal mode and another. Other researchers have found that fundamental frequency and cepstrum coefficients are also different between normal speech and shouted/whispered speech [3][4]. For our purpose of adding such features to computer music, we decide to focus on the spectral envelope and reverberation effect of generated sounds with frequency, loudness and perceived distance as predefined parameters.

For implementation, we used several sample spectral envelopes as reference data points to generate the spectral envelope under desired conditions; the data include the spectral envelope of clarinet under 3 frequencies and 3 different dynamics and was provided by University of Illinois Professor James W. Beauchamp. The main method to achieve the desired distance perception is by producing the spectral envelope of the sound at its source and adjusting reverberation effects. The majority of work lies on the former.

From the physical law of waves, we know that
Lp = LS / D2
where Lp is the perceived loudness, Ls is the loudness as imaginary sound source, and D is the assigned distance, respectively. To denote the softness or say the intensity of the sound, we have
E = c * Ls
E = c * Lp * D2
where E denotes intensity level and c is a constant coefficient. As implemented in DISSCO, Lp ranges from 0 - 256, D ranges from 0 - 1, and c is set to be 2 / 256. Thus, E ranges from 0 - 2.

Figure 1: Distribution of data points

For each data point shown in the above graph, a spectral envelope is attached with it, containing the distribution of up to 20 partials. The desired frequency and loudness may not be contained within this data set, so we do two interpolations on the amplitude of each partial, one on the frequency dimension and the other on the intensity dimension. For this reason, spectral envelopes can only be generated within a specific range of frequency which the dataset contains.

The amplitude of a partial with assigned E and frequency is decided by the four data points surrounding it. The interpolation for intensity is linear and results in two values of same intensity but of different frequencies. Thus there are two data points (freq1, value1) and (freq2, value2), where we know the desired frequency and want to find out the corresponding value. Since frequency follow a power-of-two distribution, we develop a model such that
value = a * 2(b - freq1)
where value is the amplitude of each partial of a sound and a, b are coefficients.

Calculating the coefficients from the know data points, we come up with a function describing the relationship between frequency and value in this particular range and acquire the desired value. An envelope is applied to every partial which simulates the attack, sustain and decay phase of a sound.

Another important factor that has noticeable influence on perceived distance, reverberation effects, has not gone through careful study. Although simulation of reverberation effects are already implemented in DISSCO, some specific model and parameters may be required to generate the effect that adjust the perceived distance. Our future work includes thorough study of reverberation effects’ influence on perceived distance and transition from such study to implementation in DISSCO.

Based on our current work, there are still many potential developments and improvements. For one, our current samples has a limited range of frequency and only represents the spectral envelope of one instrument. In the future, we are planning to collect more data points for a wider range and smaller subdivision of frequency; spectral envelope of other instruments should be present as well. Furthermore, we can allow users to input the value for spectral envelope data points as they prefer.

Automatic notation of randomly generated sounds.
The automatic notation module allows DISSCO to generate score files that can be printed in pdf format with the help of Lilypond, an open-source software. Due to the difference between sound/note representation in DISSCO and Lilypond's requirements, automatic notation module has to convert the output of the composition process into an input file that can be recognized by Lilypond. The module resides in CMOD and is accessed through Bottom, the lowest node of the tree structure. It performs three main functions: organizes all notes and rests in an ordered sequence; insures that all rhythmic features are compatible with Western notation symbols; converts individual notes and creates an output file.
1. Notes organization
When using certain DISSCO features, sounds are computed in a random order and a note that is in the middle of the piece might be generated as the first one while the first note of the piece could be produced last. However, traditional western notation lists the notes of a piece in the sequence in which they are going to be performed. In the automatic notation module, two vectors are used to store and organize the data. As notes are generated, they are inserted into the first vector. After all the notes are created, the program will loop through the first vector, sort the sounds according to their start time and insert the rests created by the gaps between them into the second vector. When the second vector is filled with notes and rests, the program outputs the processed data to a file.
2. Rhythmic modifications
CMOD, the composition module, allows only start and end times that can be written when employing traditional Western notation symbols no matter what subdivisions of the beat or "tuplets" are present. This is accomplished by defining an Elementery Displacement Unit or EDU as 1 / LCM (Lowest Common Multiple) of the numbers representing such subdivisions. As an example, if divisions by 2 (eight notes), 4 (sixteenth notes), 5 (quintuplets) and 6 (sextuplets) are used, EDU = 1 / 3*4*5 and the beat has a size of 60 EDUs. However not all EDU values between 0 and 60 can be represented: only 10, 12, 15, 20, 24, 30, etc. EDUs corresponding to multiples of 60 / 6, 60 / 5, 60 / 4, etc. can be. The valid elements are selected with the help of sieves , logical filters based on modulo and Boolean operations [5].

Due to the fact that silences/rests are inserted at a later time, problems may arise if one type of tuplet is assigned at the beginning of a beat (eg. a sixteenth note, 15 EDUs) and another type begins during the duration of the same beat (eg. last two parts of a quintuplet starting at 36 EDUs). In that case, the duration of the rest is 21 EDUs for which Western notation does not provide a symbol. In such cases, when an invalid duration is encountered, the program will modify its end time along with the start time of the following sound, to make sure all the notes fit in the criteria of traditional notation. When modifying the values, the program will try to minimize the changes to preserve the original situation as much as possible.

The traditional western notation has limited types of notes: whole note, half note, quarter note, eighth note, and so forth along with their dotted counterparts. The next step is to select the best basic type of notes and their associated symbols that best represent the assigned durations. In the case of durations longer than a beat or even one bar the automatic notation system has to decide which is the best way of dividing the sound over many beats or bars and drawing the appropriate ties.

3. Data conversion
Note attributes - start time, duration, pitch, dynamic mark, articulation, etc. - represented initially as integer numbers need to be changed into symbols used by Lilypond. Specifically, in the printing software, " c ", " d ", " e ", … , " b " denote pitches and commas or single quotation marks are used to show the octave. For example, C4, with the value of 48 becomes the string " c ", and C5, of value 60, the string "c' ". In converting pitches, the octave index ia given by the value divided by 12, and the pitch index or the pitch class by the value modulo 12. The octave index and pitch index are looked up from the tables and the string representing the pitch is stored into a variable within the Note class.
The perceived loudness is a subjective magnitude expressed in sones on a scale with powers of 2 values between 0 - 256 that corresponds to traditional dynamic markings such as " pp ", " f " or " mf ". The program determines the range in which the computed number falls and assigns the closest marking. For articulations and all other indications the interface, LASSIE, allows the user to select Lilypond symbols representing values at predefined parameters.
The final results are stored in an .ly input file for Lilypond.
Evolutionary music.
This computation model deals with a piece of music in a state of flux, iteratively changing its structure and sound attributes in order to approach a parameterized destination. When these changes are driven using Information Theoretical concepts, this model closely resembles the Create-Analyze-Modify workflow cycle of human music composition.

In DISSCO a piece of music is comprised of a number of events – Top, High, Medium, Low and Bottom. The events represent various structural levels of the piece – sections, themes, chords etc. A musical piece is represented by a directed graph of event nodes, rooted at the unique top event.
This graph structure, together with the ability incorporate randomness at every level, makes it possible to create evolving pieces of music.

Information Theory Concepts (Not sure if this is general knowledge or if we need this)

1. Shannon Entropy	H = -∑_(i=1)^(i=n)▒〖log⁡(p_i )∗p_i 〗

2. Redundancy	H_max – H

(To be done..)
(Some explanation of the functions you use in DISSCO like RandomInt, Stochos, etc and how we use Monte Carlo method to estimate probabililty distribution for nested functions.)

We used an Evolutionary Algorithm to model the human composition workflow. The main steps of the algorithm are:

1. Partitioning: Group event nodes by type and also by their role in the musical structure. For example, we could group nodes corresponding to the same musical section, instrument, event type and so on. This offers limited control of the modifications made to the piece during the evolution process.

2. Evaluation: The main idea behind using Information theoretic concepts and mathematical aesthetic measures in the evaluation process is to make it as objective as possible. In 1933 George Birkhoff devised an objective way to describe the aesthetic experience, proposing that an aesthetic measure is the ratio between Order and Complexity. While his theory was primarily notional, many mathematical interpretations of that idea have been proposed over the past few decades. For example, Bense and Moles propounded that the ideal aesthetic measure was the ratio between redundancy and information, Machado and Cardoso claimed that it was the ratio between Piece Complexity and Processing Complexity, and so on.

While most of the above mentioned interpretations we designed to be applied to visual art, we believe that given DISSCO’s large capacity to incorporate randomness and the broad utility of Information Theory, some of these designs can be applied to computer music as well.

In our algorithm, the aesthetic measure acts as a fitness function. After the user selects an aesthetic measure and their optimum measure value, we compute the local aesthetic value for each of the event nodes in our partition. In addition to the event attribute data, we use Shannon Entropy to quantify the amount of information in an event. The Parents are then chosen using fitness proportionate selection.

3. Crossover:We combine the attributes from the two parent events to form the child node. The least fit event node in the partition is replaced by the newly created child.
.
4. Mutation: Alter one or more attribute values so as to maintain diversity and prevent premature convergence. There is a strong emphasis on exploration as opposed to straightforward optimization, as the transitory pieces created in the process are of much value to the composer. The evolution computations can continue for an arbitrary length of time, but it can be paused by the composer if he or she wants to listen to the transient piece.

5. Repeat steps 2 - 4 till the global Aesthetic Measure for the whole piece approaches the user defined optimum.

(For the Future work section)
However this is very much a work in progress. Presently, only the loudness and frequency attributes are considered in the entropy calculation. Future work may include incorporating other attributes into the aesthetic measure, looking into adaptive genetic algorithms and updating the user interface to allow customized weighting for the different attributes.

An appropriate question remains: why high-performance computing is necessary for pursuing a musical project ? The answer becomes obvious if we consider the fact that the final audio file consists of at least 44,100 digital samples for every second (the present CD standard) and that involved computations are necessary for the creation of each sound. Moreover, computation time should be equal or less to real time (the time needed to listen to the result) especially in the case of the Evolving Entity model that requires thousands of iterations. As an example, a recent eight minutes piece including over 770,000 sounds was produced in almost real time at the San Diego Supercomputing Center where where a parallel version of the code is implemented.

  The recent additions to DISSCO discussed above emphasize the interdisciplinary aspect of the project which resides at the intersection of scientific concepts and music composition, a collaboration facilitated by technology.

References
1. Kaper, H. G. and Tipei, S., "DISSCO: A Unified Approach to Sound Synthesis and Composition",	Proc. of the 2005 Int'l Computer Music Conference, Barcelona, Spain, 2005.
2. Zhang, C., and Hansen, J. "Analysis and Classification of Speech Mode: Whispered through	Shouted". Proc. Interspeech. doi:10.1.1.668.5520.
3. Itoh, T., Takeda, K., & Itakura, F. (n.d.). "Acoustic analysis and recognition of whispered	speech". IEEE Workshop on Automatic Speech Recognition and Understanding, 2001. ASRU	01.doi:10.1109/asru.2001.1034676.
4. Raitio, T., Suni, A., Pohjalainen, J., Airaksinen, M., Vainio, M., & Alku, P. (2013). "Analysis and	Synthesis of Shouted Speech". INTERSPEECH 2013, 14th Annual Conference of the	International Speech Communication Association. Retrieved August 10, 2018.
5. Tipei, S., "Composing with Sieves: Structure and Indeterminacy In-Time", Proc. of the 2013 Int'l	Computer Music Conference, Perth, Australia, 2013.
6. Tipei, S., "Composition as an evolving entity an experiment in progress". Proc. of the 2016 Int'l	Computer Music Conference, Utrecht, The Netherlands, 2016.
7. Birkhoff, G. D., Aesthetic Measure, Harvard Univ. Press, 1933.
8. Bense, M., Einführung in die informationstheoretische Asthetik.
 Grundlegung und Anwendung in der Texttheorie, Rowohlt Taschenbuch Verlag, 1969.
10. Machado, Penousal & Cardoso, Amílcar. Computing Aethetics, 1515. 219-228.	10.1007/10692710_23.
11. Rigau, J., Feixas, M., and Sbert, M.,“Conceptualizing Birkhoff’s Aesthetic Measure Using	Shannon Entropy and Kolmogorov Complexity,” Proc. Eurographics Workshop Computational	Aesthetics in Graphics, Visualization and Imaging, Eurographics Assoc., 2007, pp. 105-112
12. Moles, A., Information Theory and Esthetic Perception, Univ. of Illinois Press, 1968.